## Slide 1: Introduction to Microcontrollers Fall Term, 2021
Professor Allan Douglas

## Slide 2: Schedule/Labs
Lab#3
  Due tonight by midnight.
Lab#4 has been posted on Canvas.
  Due 11/9 by midnight.

## Slide 3: Lecture Outline
Lab Reports
Interrupts
  Interrupt Unit
  Internal vs. External Interrupts
  Interrupt Service Routines
Timer/Counters
  Resources available in ATMega 328P
  Control Registers
  Prescaling
  Use Cases
Lab#4
  Overview

## Slide 4: Lab Report Rubric
Category | % Possible | Description of Criteria
Presentation/Clarity | 10 | Neatly formatted presentation of material Clear sentences with coherent flow Readable and properly labeled figures/tables
Introduction | 5 | Purpose and overall objective(s) stated
Procedure/Results | 70 | Procedure clearly described Code provided and commented when appropriate All required work from checklist included and discussed All included figures/tables referenced in text
Summary/Conclusion | 15 | Experience and challenges discussed Understanding of material demonstrated
Total | 100 | 

## Slide 5: Atmega328P Block Diagrams
ATmega328P Data Sheet, downloaded from http://www.atmel.com
32kBytes

## Slide 6: Interrupt versus Polling
Setup()
Loop()
  Command
  Command
  Command
  Command
  Command
Interrupt Service Routine (ISR)
  Interrupt Command
  Interrupt Command
  Interrupt Command
Interrupt
Event

## Slide 7: AVR 328P Interrupts
1 Reset
2 External Interrupt Request 0 (pin D2) (INT0_vect)
3 External Interrupt Request 1 (pin D3) (INT1_vect)
4 Pin Change Interrupt Request 0 (pins D8 to D13) (PCINT0_vect)
5 Pin Change Interrupt Request 1 (pins A0 to A5) (PCINT1_vect)
6 Pin Change Interrupt Request 2 (pins D0 to D7) (PCINT2_vect)
7 Watchdog Time-out Interrupt (WDT_vect)
8 Timer/Counter2 Compare Match A (TIMER2_COMPA_vect)
9 Timer/Counter2 Compare Match B (TIMER2_COMPB_vect)
10 Timer/Counter2 Overflow (TIMER2_OVF_vect)
11 Timer/Counter1 Capture Event (TIMER1_CAPT_vect)
12 Timer/Counter1 Compare Match A (TIMER1_COMPA_vect)
13 Timer/Counter1 Compare Match B (TIMER1_COMPB_vect)
14 Timer/Counter1 Overflow (TIMER1_OVF_vect)
15 Timer/Counter0 Compare Match A (TIMER0_COMPA_vect)
16 Timer/Counter0 Compare Match B (TIMER0_COMPB_vect)
17 Timer/Counter0 Overflow (TIMER0_OVF_vect)
18 SPI Serial Transfer Complete (SPI_STC_vect)
19 USART Rx Complete (USART_RX_vect)
20 USART, Data Register Empty (USART_UDRE_vect)
21 USART, Tx Complete (USART_TX_vect)
22 ADC Conversion Complete (ADC_vect)
23 EEPROM Ready (EE_READY_vect)
24 Analog Comparator (ANALOG_COMP_vect)
25 2-wire Serial Interface (I2C) (TWI_vect)
26 Store Program Memory Ready (SPM_READY_vect)
(VALUE) is the name of the interrupt vector.

## Slide 8: Arduino Pinout & External Interrupts
External
Interrupts

## Slide 9: AVR 328P External Interrupts

## Slide 10: AVR 328P External Interrupts
ISR = Interrupt Service Routine
  This is a function that is automatically called when an interrupt occurs.

## Slide 11: Arduino Commands to Handle Interrupts
interrupts() : global interrupt enable
noInterrupts() : global interrupt disable
attachInterrupt() : Associate an external interrupt with an ISR
detachInterrupt() : Disconnect the ISR
When an interrupt occurs, a flag in the interrupt flag register (TIFRx) is set.
This flag is automatically cleared when entering the ISR.
https://arduino-info.wikispaces.com/Timers-Arduino

## Slide 12: Interrupt Service Routines (ISRs)
Interrupt reference links:
  http://gammon.com.au/interrupts
  http://letsmakerobots.com/content/arduino-101-timers-and-interrupts
When writing an Interrupt Service Routine (ISR):
  Keep it short
  Don't use delay ()
  Don’t include serial prints statements (these functions are very slow)
  Make variables shared with the main code volatile
  Don't try to turn disable interrupts in an ISR
Volatile variable declaration forces the compiler to re-read the value when used because an external source (ISR) may have changed the value of the variable.

## Slide 13: ISR Example Code
Volatile
20Hz
ISR

## Slide 14: Microcontroller Counter/Timers
Many applications need to count events or generate time delays.
The ATmega 328P has the following hardware resources:
  Timer/Counter0: 8-bits (max. count is 255)
    This Timer is used for the Arduino delay(), millis(), and micros() functions.
  Timer/Counter1: 16-bits (max. count is 65535)
  Timer/Counter2: 8-bits (max. count is 255)
    This timer is almost identical to Timer0 except that Timer2 can be used as a real time counter with an additional external 32.768kHz crystal.
    There are also a few differences in their control registers.
Timers can be configured in different modes:
  Normal mode.
  PWM mode. (Pulse width modulation mode.): the OCxy outputs are used to generate PWM signals.
  CTC mode. Clear timer on compare match. When the timer counter reaches the compare match register, the timer will be cleared.
  PWM, phase correct mode.
  Fast PWM mode.

## Slide 15: 8-bit Counter/Timer0/2
8-bit counter
8-bit register
8-bit register
5 Registers to control and interface with the timer.
8-bit register
8-bit register
Prescaler

## Slide 16: External Timer Inputs
Logic Synchronizer
To Counter clock enable
These inputs can be used to count external events (edges)

## Slide 17: Timer/Counter0 Control Registers
TCNT0: 8-bit up/down, loadable counter with reset.
TCCR0A: Control Register A (compare and mode bits)
TCCR0B: Control Register B (prescaler and mode bits)
OCR0A: Output Compare Register A
OCR0B: Output Compare Register B
TIMSK0 - Timer/Counter Interrupt Mask Register. To enable/disable timer interrupts.
TIFR0 - Timer/Counter Interrupt Flag Register. Indicates a pending timer interrupt.

## Slide 18: Timer Interrupts
Timer Overflow: Timer overflow means the timer has reached is limit value. When a timer overflow interrupt occurs, the timer overflow bit TOVx will be set in the interrupt flag register TIFRx. When the timer overflow interrupt enable bit TOIEx in the interrupt mask register TIMSKx is set, the timer overflow interrupt service routine ISR(TIMERx_OVF_vect) will be called.
Output Compare Match: When a output compare match interrupt occurs, the OCFxy flag will be set in the interrupt flag register TIFRx . When the output compare interrupt enable bit OCIExy in the interrupt mask register TIMSKx is set, the output compare match interrupt service ISR(TIMERx_COMPy_vect) routine will be called.

## Slide 19: Timer/Counter0 Interrupt Flags

## Slide 20: Timer/Counter0 Interrupt Mask

## Slide 21: Controlling Timer0
Control of Prescaler
Control of Mode. OC0A/B toggle,
set, or clear on match.
Control of counting sequence,
maximum counter value, type of waveform generation (PWM).
Force Output Compare

## Slide 22: Timer Interrupts
Timer Overflow: Timer overflow means the timer has reached is limit value. When a timer overflow interrupt occurs, the timer overflow bit TOVx will be set in the interrupt flag register TIFRx. When the timer overflow interrupt enable bit TOIEx in the interrupt mask register TIMSKx is set, the timer overflow interrupt service routine ISR(TIMERx_OVF_vect) will be called.
Output Compare Match: When an output compare match interrupt occurs, the OCFxy flag will be set in the interrupt flag register TIFRx . When the output compare interrupt enable bit OCIExy in the interrupt mask register TIMSKx is set, the output compare match interrupt service ISR(TIMERx_COMPy_vect) routine will be called.
Timer Input Capture (only supported on Timer1): When a timer input capture interrupt occurs, the input capture flag bit ICF1 will be set in the interrupt flag register TIFR1. When the input capture interrupt enable bit ICIE1 in the interrupt mask register TIMSK1 is set, the timer input capture interrupt service routine ISR(TIMER1_CAPT_vect) will be called.

## Slide 23: Timer1 Input Capture Registers

## Slide 24: Timer Prescaler
16 MHz
External
pins.
0
7
0
7

## Slide 25: Timer0 Prescaler Control Bits
Prescaling allows you to control the time between counter increments.
You can increase the time between counter overflow events, but the time steps become more coarse.

## Slide 26: Examine the Timer Registers

## Slide 27: A Closer Look at Timer0
TCCR0B = 0x3
  CS01 and CS00 are set
  Prescaler = 64
Microcontroller clock rate is 16MHz
Counter increments once every 64*T = 64/16MHz = 4us
Counter will count to 256*4us = 1.024ms
millis() - Returns the number of milliseconds since the program started
  (unsigned long = 32 bits)
The number of milliseconds since the Arduino board began running the current program. This number will overflow (go back to zero), after approximately 50 days.
  2^32-1 = 4,294,967,295 * 1.024ms = 439,8046s = 50.903316 days
micros() - Returns the number of microseconds since the Arduino board began running the current program. This number will overflow (go back to zero), after approximately 70 minutes.

## Slide 28: 16-bit Counter/Timer1
16-bit counter
16-bits
16-bits
T1

## Slide 29: Timer/Counter1 Control Registers

## Slide 30: Timer/Counter1 Count Register

## Slide 31: Timer1 Registers
File: iom328p.h
#define TCCR1A _SFR_MEM8(0x80)
#define WGM10 0
#define WGM11 1
#define COM1B0 4
#define COM1B1 5
#define COM1A0 6
#define COM1A1 7
#define TCCR1B _SFR_MEM8(0x81)
#define CS10 0
#define CS11 1
#define CS12 2
#define WGM12 3
#define WGM13 4
#define ICES1 6
#define ICNC1 7
#define TIMSK1 _SFR_MEM8(0x6F)
#define TOIE1 0
#define OCIE1A 1
#define OCIE1B 2
#define ICIE1 5
Bitwise xor
Alternative method to write your ISR. Use this technique for Lab#4.
See slide 7

## Slide 32: Enabling Interrupt Masks
When working with interrupts as shown in the previous slide, make sure that you enable the interrupt mask register as follows:
EIMSK |= (1 << INT0); // Turns on INT0

## Slide 33: What does this code do?
Count up to 31,250
Prescaler = 256, so T = 256/16MHz = 16us
So, ledPin high time = 31,250 * 16us = 0.5 seconds
Timer1 is 16-bits

## Slide 34: Excellent Reference on Timers
A copy of an article from Nuts & Volts magazine has been uploaded on Canvas (Week#5).
The file is called TimersArticle.pdf
I encourage everyone to read it.

## Slide 35: Lab#4
Part 1: Interrupt Speed Test
  Connect the function generator to an interrupt input on the Arduino and write a sketch to respond to external interrupts. Determine mazimum rate possible for handling interrupts.
Part 2: Measuring Pulse Duration
  Measure the duration of a function generator pulse using the micros() function and interrupts. Then you will repeat the process with a timer.
Let’s review the Lab#4 assignment document.