## Slide 1: Introduction to Microcontrollers Fall Term, 2021
Professor Allan Douglas

## Slide 2: Schedule/Labs
Lab#5
  Due by midnight.
Lab#6 has been posted on Canvas.
  Due 11/23 by midnight

## Slide 3: Lecture Outline
Analog Comparators
  Comparator Concepts
Atmega328P Analog Comparator
  Control Registers
  Interrupts
  Arduino Commands
Analog to Digital Converter (ADC)
  ADC Concepts
  Successive Approximation, Resolution/Accuracy
Atmega328P Analog to Digital Converter
  Bandgap Reference
  Control Registers
  Acquisition Time/Sampling Rate Limitations
  Interrupts
  Arduino Commands
Lab#6

## Slide 4: Analog Comparators
Analog Comparator is a module that compares two analog input voltages and outputs a signal level indicating which of the inputs is greater or lesser.
An analog comparator is basically an amplifier (op-amp) without feedback and thus has very high gain.
http://embedded-lab.com/blog/?p=10522

## Slide 5: Atmega328P Pinout
Analog
Comparator
Inputs
Analog
Converter
Inputs

## Slide 6: Analog Comparator
The Analog Comparator compares the input values on the positive pin AIN0 and negative pin AIN1.
When the voltage on the positive pin AIN0 is higher than the voltage on the negative pin AIN1, the Analog Comparator output, ACO, is set.
The comparator’s output can be set to trigger the Timer/Counter1 Input Capture function.
In addition, the comparator can trigger a separate interrupt, exclusive to the Analog Comparator.
The user can select Interrupt triggering on comparator output rise, fall or toggle.
Transmission
Gate

## Slide 7: Comparator Control Registers

## Slide 8: Comparator Control Registers

## Slide 9: Comparator Control Registers

## Slide 10: Analog to Digital Converters (ADCs)
Everything in the physical world is analog.
We use a transducer (sensor) to convert physical quantities to an electrical signal (voltage or current).
ADCs are used to convert an analog voltage or current into a digital representation for processing.
Some physical quantities what we may want to measure are:
  Voltage, current, power, magnetic field strength
  Temperature, wind pressure, air pressure, humidity, flow rate
  Velocity, angular velocity, acceleration
  Light intensity
Transducer Types
  Electromagnetic, electrochemical, electromechanical, electroacoustic, photoelectric, electrostatic, thermoelectric, radio acoustic
https://en.wikipedia.org/wiki/Pulse-width_modulation

## Slide 11: ADC Devices
Resolution
  ADCs have n-bit resolution, where n can be 8, 10, 12, 16 or even 24 bits.
  For a 10-bit ADC, the sampled values will be between 0-1023
Reference Voltage
  ADCs require a precise reference voltage.
  The ATmega328P has 3 different references available.
Conversion Time
  The conversion time depends on the technique used for conversion.
  The ATmega328P uses a technique called successive approximation.

## Slide 12: Analog-to-Digital Converter Block Diagram
The ATmega328P has a 10-bit ADC
The ADC has a MUX to select 1 of 8 different inputs.
  The DIP package version of the chip only supports 6 inputs.
  The UNO only supports 6 inputs even if you have the SMT component.
The ADC contains a Sample and Hold circuit which ensures that the input voltage to the ADC is held at a constant level during conversion.

## Slide 13: Voltage Reference Options
Fixed Bandgap Voltage Reference
  A bandgap voltage reference is a temperature independent voltage reference circuit widely used in integrated circuits.
  It produces a constant voltage regardless of power supply variations, temperature changes and circuit loading from a device.
Internal 1.1V Reference
  The internal 1.1V reference is generated from the internal bandgap reference (VBG) through an internal amplifier.
External AVCC Reference
  The ADC has a separate analog supply voltage pin, AVCC.
  AVCC must not differ more than ±0.3V from VCC.
  The voltage reference may be externally decoupled at the AREF pin by a capacitor for better noise performance.
External AREF Reference
  Externally provided by the PCB designer.

## Slide 14: Arduino UNO Schematic
External
Reference
AVCC is +5V
Analog
Comparator
Inputs
Analog
Inputs

## Slide 15: Successive Approximation
The ADC converts an analog input voltage to a 10-bit digital value through successive approximation.
The minimum value represents GND and the maximum value represents the voltage on the AREF pin minus 1 LSB.
To perform a conversion the microcontroller performs the following steps:
  Set an internal voltage (Digital to Analog Converter - DAC)
  Compares internal voltage to the held sample
  Adjust the internal voltage
  Repeat steps 1-3 until the difference is minimized
This process is iterative, so it takes 13 prescaled clock cycles to complete.
  First conversion requires 25 prescaled clock cycles (initialization)
  Subsequent conversions take 13 prescaled clock cycles

## Slide 16: Internal Temperature Sensor
Process variation causes the output voltage from the temperature sensor to vary from one chip to another.
To enable more accurate results, the temperature measurement can be calibrated in the application software.
This software calibration requires that a calibration value is measured and stored in EEPROM for each chip.

## Slide 17: ADC Control Registers

## Slide 18: ADC Control Registers

## Slide 19: ADC Control Registers
Not available in Arduino UNO
Not available in Arduino UNO
Not available in Arduino UNO

## Slide 20: ADC Control Registers

## Slide 21: ADC Control Registers

## Slide 22: ADC Control Registers
Note: The maximum conversion rate is 200kHz for an Atmega328P.

## Slide 23: ADC Control Registers
The ADC has 10-bit resolution.

## Slide 24: ADC Control Registers

## Slide 25: ADC Control Registers

## Slide 26: ADC Control Registers

## Slide 27: Arduino Example #1
Read from ADC with MUX
set to pin A0.
analogRead(pinNumber);

## Slide 28: Arduino Example#2
Reads an analog input pin
Maps the result to a range from 0 to 255
Uses the result to set the pulse width modulation (PWM) of an output pin.
Prints the results to the serial monitor.
PWM duty cycle
for analogWrite()
ADC for analogRead()

## Slide 29: Lab#6
Part 1: DC Voltage Measurement
Write an Arduino sketch to measure the ADC0 input, scale your ADC measurement so that full range corresponds to 5V (set your reference to Vcc), and display the voltage on your LCD and on the Serial Monitor. Determine how many digits you should display beyond the decimal point based on the ADC accuracy.
Part 2: AC Voltage Measurement
Write an Arduino sketch to measure the ADC1 input. Connect a function generator to your microcontroller ADC1 input. Setup the function generator to generate a 10Hz sine wave with an amplitude of 2.5V with a +2.5V offset. Set your sampling rate to 125kHz and use Free Running mode. Write your code to determine the minimum voltage, the maximum voltage, and the period. Display your results on the Serial Monitor every second. This is challenging.
Part 3: Temperature Measurement
Write a sketch to measure two temperatures per second. You may use the delay() function for this. Your sketch should set the ADC input MUX to the internal temperature reference, start a measurement, and wait for the conversion complete interrupt. Then read the ADC data registers, set the ADC input MUX to the pin ADC0 (external temperature sensor), start a measurement, and wait for the conversion complete interrupt.
Now, convert both temperatures to degrees C. Determine how many digits you should display beyond the decimal point based on the ADC accuracy. Display both measurements on the Serial Monitor.