## Slide 1: Introduction to Microcontrollers Fall Term, 2021
Professor Allan Douglas

## Slide 2: Schedule/Labs
Lab#6
  Due by midnight.
Lab#7 has been posted on Canvas.
  Due 11/30 by midnight

## Slide 3: Lecture Outline
IR Remote Transmission and Reception
  IR Concepts
  IR Components
  IR Remote Library
  Pulse Code Modulation
Lab#7

## Slide 4: IR Communications Concepts
IR remote control systems utilize Pulse Code Modulation (PCM), where the modulating carrier frequency typically resides in the range 30kHz to 58kHz.
Modulation means turning the IRLED on and off rapidly in bursts of the carrier frequency.
The receiver is tuned to this carrier frequency, ensuring that it receives only the signal required. It then uses this frequency to demodulate the signal.
When the IRLED is not emitting light, the transmitter is in the OFF state, which in terms of the signal is referred to as a 'space'. During IRLED activity, where the light is emitted in pulsed fashion at the carrier frequency, the transmitter is in the ON state, which is referred to as a pulse or 'mark'.
At the receiver, a 'space' is output as a High, while a mark is output as a Low.
These spaces and marks are not the '0's and '1's of the command being transmitted, however. The actual data to be sent from the controller is encoded. The method of encoding used determines how to represent the '1's and '0's in terms of the marks and spaces.
http://techdocs.altium.com/display/FPGA/Infrared+Communication+Concepts

## Slide 5: IR Communications Components
IR LED
IR Sensor

## Slide 6: IR Applications
IR Communications
  TVs, BlueRay Players, Stereos
  Universal Remotes
Presence Sensing
  Robot collision detection
  Reflective sensors for hand dryers, towel or soap dispensers, water faucets, toilet flush
  Vending machine fall detection
  Security and pet gates
  Person or object vicinity activation

## Slide 7: Encoding
The following three methods of encoding are typically used in IR remote control systems.
Pulse Distance Encoding
Pulse Length Encoding
Manchester Encoding
38.222kHz pulses

## Slide 8: IR Arduino Library
Thanks to Ken Shirriff
  http://www.righto.com/2009/08/multi-protocol-infrared-remote-library.html
This IR remote library lets you both send and receive IR remote codes in multiple protocols.
It supports NEC, Sony SIRC, Philips RC5, Philips RC6, and raw protocols.
If you want additional protocols, they are straightforward to add.
The library can even be used to record codes from your remote and re-transmit them, as a minimal universal remote.
Installation
1. Navigate to the [Releases](https://github.com/z3t0/Arduino-IRremote/releases) page.
2. Download the latest release.
3. Extract the zip file
4. Move the "IRremote" folder that has been extracted to your libraries directory.
5. Make sure to delete Arduino_Root/libraries/RobotIRremote. Where Arduino_Root refers to the install directory of Arduino. The library RobotIRremote has similar definitions to IRremote and causes errors if both are installed.

## Slide 9: NEC IR Remote Protocol
Modulation frequency is 38.222kHz
The NEC IR transmission protocol uses pulse distance encoding of the message bits.
Each pulse burst (mark – RC transmitter ON) is 562.5µs in length, at a carrier frequency of 38kHz (26.3µs).
Logical bits are transmitted as follows:
  Logical '0' – a 562.5µs pulse burst followed by a 562.5µs space, with a total transmit time of 1.125ms
  Logical '1' – a 562.5µs pulse burst followed by a 1.6875ms space, with a total transmit time of 2.25ms
http://techdocs.altium.com/display/FPGA/NEC+Infrared+Transmission+Protocol

## Slide 10: NEC IR Remote Protocol
When a key is pressed on the remote controller, the message transmitted consists of the following, in order:
  a 9ms leading pulse burst (16 times the pulse burst length used for a logical data bit)
  a 4.5ms space
  the 8-bit address for the receiving device
  the 8-bit logical inverse of the address
  the 8-bit command
  the 8-bit logical inverse of the command
  a final 562.5µs pulse burst to signify the end of message transmission.
  The four bytes of data bits are each sent least significant bit first.

## Slide 11: NEC IR Remote Protocol
  The format of an NEC IR transmission frame, for an address of 00h (00000000b) and a command of ADh (10101101b).
Notice that it takes:
  27ms to transmit both the 16 bits for the address (address + inverse) and the 16 bits for the command (command + inverse). This comes from each of the 16 bit blocks ultimately containing eight '0's and eight '1's - giving (8 * 1.125ms) + (8 * 2.25ms).
  67.5ms to fully transmit the message frame (discounting the final 562.5µs pulse burst that signifies the end of message).

## Slide 12: NEC IR Remote Protocol
REPEAT CODES
If the key on the remote controller is continually depressed, a repeat code will be issued, typically around 40ms after the pulse burst that signified the end of the message. A repeat code will continue to be sent out at 108ms intervals, until the key is finally released.
The repeat code consists of the following, in order:
  a 9ms leading pulse burst
  a 2.25ms space
  a 562.5µs pulse burst to mark the end of the space (and hence end of the transmitted repeat code).
This figure illustrates the transmission of two repeat codes after an initial message frame is sent.

## Slide 13: Real Example: Address/Command
This is the On/Off button from a Frigidaire AC unit.
0001_0000_1010_1111_1000_1000_0111_0111 = 0x10AF8877
~9ms
Signal is inverted

## Slide 14: IRrecvDumpV2
Serial Monitor Output
Encoding : NEC
Code : 10AF8877 (32 bits)
Timing[67]:
+9000, -4350 + 650, - 450 + 700, - 450 + 650, - 450
+ 650, -1550 + 650, - 500 + 650, - 450 + 650, - 450
+ 650, - 450 + 700, -1550 + 600, - 500 + 650, -1550
+ 650, - 450 + 700, -1550 + 600, -1600 + 650, -1600
+ 600, -1600 + 650, -1600 + 600, - 500 + 650, - 450
+ 700, - 400 + 700, -1550 + 600, - 500 + 650, - 450
+ 700, - 400 + 700, - 400 + 700, -1550 + 600, -1600
+ 650, -1600 + 650, - 450 + 700, -1550 + 600, -1600
+ 650, -1550 + 650
unsigned int rawData[67] = {9000,4350, 650,450, 700,450, 650,450, 650,1550, 650,500, 650,450, 650,450, 650,450, 700,1550, 600,500, 650,1550, 650,450, 700,1550, 600,1600, 650,1600, 600,1600, 650,1600, 600,500, 650,450, 700,400, 700,1550, 600,500, 650,450, 700,400, 700,400, 700,1550, 600,1600, 650,1600, 650,450, 700,1550, 600,1600, 650,1550, 650}; // NEC 10AF8877
unsigned int data = 0x10AF8877;

## Slide 15: Extended NEC Protocol
The first two bytes are not bitwise inverses. Why is this?
The NEC protocol has been so widely used that all possible addresses were used up.
By sacrificing the address redundancy, the address range was extended from 256 possible values to approximately 65536 different values.
This way the address range was extended from 8 bits to 16 bits without changing any other property of the protocol.
By extending the address range this way the total message time is no longer constant.

## Slide 16: Real Example: Repeat Codes
On/Off button from a Frigidaire AC unit held down.
108ms period

## Slide 17: Lab#7
Part 1: IR Communications
Part 2: Arduino Communications with IR
  Two microcontrollers communicating with IR signals.
  Use your Arduino board and the breadboard microcontroller you built in Lab#1.
IR Receiver Diode
LED - Infrared 950nm