## Slide 1: Introduction to Microcontrollers Fall Term, 2021
Professor Allan Douglas

## Slide 2: EE333 - Course Instructor
Associate Professor: Allan Douglas
Email: allan.douglas@oit.edu
BSEE Oregon State University 1991
MSEE Oregon State University 1993
28 years of industry experience
  Digital System Design/Architecture
  Field Programmable Gate Arrays (FPGA)
  Microprocessors/Microcontrollers
  VHDL/Verilog
  High-Speed Circuit Boards

## Slide 3: EE333 - Description and Prerequisites
Course Description
  Microcontroller engineering using popular microcontroller, internal structures and control units, timing, interrupts, memory interfacing, assembly language programming specific to microcontroller, and on-chip peripheral devices.
Prerequisites CST 116
Corequisites CST 133 or EE 133 or EET 216

## Slide 4: EE333 - Lab Work
Labs
  The list of required components is available on Canvas.
  There will be 8 labs this term.
  Labs may provide opportunities for students to earn extra credit. Extra credit will be work 5%. If students desire to go further with lab work, they may gain more than 5% extra credit with instructor approval.
  Students will work independently.
  Students will have one week to complete each lab.
  Each student will submit a Lab Report.
  Late Lab Reports will be penalized 5% per day late.
  Lab Reports submitted more than 7 days after the due date will not be accepted.
Extra Credit Lab
  At the end of the term, we may have time for an extra credit lab.
  Please talk to the instructor if you are interested.

## Slide 5: EE333 - Grading
Homework and Exams
  This course does not have homework assignments or exams. Instead, the course consists of extensive hands-on, lab work.
Grading
  Lab Reports 100% (each is worth 12.5%)

## Slide 6: EE333 – Textbook(s)
Arduino Internals (Recommended)
  Dale Wheat
  ISBN: 978-1-430-23882-9
Exploring Arduino (Optional)
  Jeremy Blum, 2013
  ISBN: 978-1-118-54936-0
Beginning C for Arduino (Optional)
  Jack Purdum, 2012
  ISBN: 978-1-430-24776-0
Most material is available online.

## Slide 7: EE333 - Schedule
Week 1 - Class Syllabus/Intro to Microcontrollers/Software Tools
Week 2 - Intro to Microcontroller Programming and Tools
Week 3 - Serial Communication
Week 4 - Microcontroller Internal Structure
Week 5 – Timer/Counters & Interrupts
Week 6 – Pulse Width Modulation
Week 7 – A/D Converters and Comparators
Week 8 – Wireless Communications
Week 9 - Programming in C & Assembly
Week 10&11 – Special Topics

## Slide 8: EE333 - Lab Assignments
Lab#1: Building and Executing Code on a Microcontroller
  Breadboard prototype, Arduino IDE/Sketches, Blink, Loading Code
Lab#2: Serial Communications
  USB, RS-232, SPI, I2C
Lab#3: Digital Clock
  Liquid Crystal Displays and Real-Time Clocks with I2C
Lab#4: Timers, Counters & Interrupts
  Measuring and generating digital waveforms
Lab#5: Pulse Width Modulation
  PWM of LEDs, PWM drive of DC Motors, Stepper Motors, Servos
Lab#6: A/D Conversion and Comparators
  Temperature and signal measurement
Lab#7: Wireless Communications
  Infrared (IR) and Radio Frequency (RF) Communications
Lab#8: Assembly Programming

## Slide 9: EE333 - Lab Materials
Qty | Required | Vendor | PN | Cost
1 | Build Your Own Arduino Kit | Jameco | 2151259 | $ 14.95
1 | Arduino Uno | Arduino | UNO Rev3 | $ 24.95
1 | FTDI Basic Breakout - 5V | Sparkfun | DEV-09716 | $ 14.95
1 | IC I/O EXPANDER I2C 8B 18DIP | Digikey | MCP23008-E/P-ND | $ 1.22
1 | IC I/O EXPANDER SPI 8B 18DIP | Digikey | MCP23S08-E/P-ND | $ 1.28
1 | Basic 16x2 Character LCD - Black on Green 5V | Sparkfun | LCD-00255 | $ 13.95
1 | 10K Ohm Potentiometer | Digikey | CT6EP103-ND | $ 0.79
1 | Real Time Clock | Digikey | DS1307+-ND | $ 3.37
1 | Crystal (32.768kHz Quartz Crystal) | Digikey | 535-9034-ND | $ 0.17
1 | DC Motor | Sparkfun | ROB-11696 | $ 1.95
1 | Diode Small Signal - 1N4148 | Sparkfun | COM-08588 | $ 0.15
1 | Transistor - NPN (BC337) | Sparkfun | COM-13689 | $ 0.50
1 | Temperature Sensor - TMP36 | Sparkfun | SEN-10988 | $ 1.50
1 | LED - Infrared 950nm | Sparkfun | COM-09349 | $ 0.95
1 | IR Receiver Diode - TSOP38238 | Sparkfun | SEN-10266 | $ 1.95
1 | WiFi Module - ESP8266 | Sparkfun | WRL-13678 | $ 6.95
1 | Logic Level Converter - Bi-Directional | Sparkfun | BOB-12009 | $ 2.95
 | Total |  |  | $ 92.53
You will also need a breadboard, jumper wires, and various resistors/caps.

## Slide 10: EE333 - Software
Required
  Arduino 1.8.10 Integrated Development Environment (IDE)
    Arduino sketch development, serial comms, and download
    https://www.arduino.cc/en/Main/Software
Optional
  Atmel Studio 7.0 IDE (optional)
    Complete IDE for all Amtel products
    https://www.microchip.com/mplab/avr-support/atmel-studio-7
  WinAVR 2010_01_10 (optional)
    C compiler, linker, file conversion, programming tools
    http://sourceforge.net/projects/winavr/files/

## Slide 11: Lecture Outline
Introduction to Microcontrollers
Types and Manufactures of Microcontrollers
Introduction to the Amtel Atmega 328P Microcontroller
Arduino Boards
Software Tools (Arduino IDE)
  Libraries
  Example Code (Sketches)
Introduction to Lab#1
  Objectives and Checklist
  DIP 28 Pinout and Pin Descriptions
  Atmega 328P Datasheet/Features
Lab#1

## Slide 12: Introduction to Microcontrollers
What is a Microcontroller?
  A microcontroller (sometimes abbreviated µC, uC or MCU) is a small computer on a single integrated circuit containing a processor core, memory, and programmable input/output peripherals.
  Built-in functions/peripherals usually included are:
    Volitile Memory (SRAM)
    Non-Volitile Memory (Flash, EEPROM)
    Clock Generators
    General purpose Inout/Outputs (GPIO)
    Data Converters (ADCs and DACs)
    Timers, Event Counters, and Pulse Width Modulation (PWM) blocks
    Serial Input/Output ports (UARTs)
    Serial Interfaces (SPI, I2C, USB, CAN)
    Other Interfaces (SD card readers, Ethernet, etc.)
How is it different from a Microprocessor?
  Microcontrollers are designed for embedded applications, in contrast to the microprocessors used in personal computers or other general purpose applications.
https://en.wikipedia.org/wiki/Microcontroller

## Slide 13: What are common Microcontrollers?
As of 2008, there are several dozen microcontroller architectures and vendors including:
ARM core processors (many vendors)
  ARM Cortex-M cores are specifically targeted towards microcontroller applications
Atmel AVR (8-bit), AVR32 (32-bit), and AT91SAM (32-bit)
Cypress Semiconductor's M8C Core used in their PSoC (Programmable System-on-Chip)
Freescale ColdFire (32-bit) and S08 (8-bit)
Freescale 68HC11 (8-bit)
Intel 8051
Infineon: 8-bit XC800, 16-bit XE166, 32-bit XMC4000 (ARM based Cortex M4F), 32-bit TriCore and, 32-bit Aurix Tricore Bit microcontrollers[18]
MIPS
Microchip Technology PIC, (8-bit PIC16, PIC18, 16-bit dsPIC33 / PIC24), (32-bit PIC32)
NXP Semiconductors LPC1000, LPC2000, LPC3000, LPC4000 (32-bit), LPC900, LPC700 (8-bit)
Parallax Propeller
PowerPC ISE
Rabbit 2000 (8-bit)
Renesas Electronics: RL78 16-bit MCU; RX 32-bit MCU; SuperH; V850 32-bit MCU; H8; R8C 16-bit MCU
Silicon Laboratories Pipelined 8-bit 8051 Microcontrollers and mixed-signal ARM-based 32-bit microcontrollers
STMicroelectronics STM8 (8-bit), ST10 (16-bit) and STM32 (32-bit)
Texas Instruments TI MSP430 (16-bit) C2000 (32-bit)
Toshiba TLCS-870 (8-bit/16-bit)
https://en.wikipedia.org/wiki/Microcontroller

## Slide 14: Why Arduino for EE333?
An “Arduino” is a specific 8-bit AVR microcontroller implementation with a flash installed bootloader, the Arduino IDE and a collection of software libraries. Programs can be downloaded over USB.
  Enables us to use Arduino Sketches for code development rather than C or assembly language. Remember, the pre-requisites for EE333?
  Establishes a standard hardware platform for connecting peripherals and “shields”.
  Hardware is cheap, software is free, a special programmer is not required, and there is a massive amount of online documentation.

## Slide 15: There are 100’s of shields available!

## Slide 16: Arduino UNO
Atmel ATmega328P
microcontroller
Serial port
USB-to-Serial Chip

## Slide 17: Arduino Uno R3/SparkFun RedBoard Pinouts
DIP Package
SMT Package
Std USB
Micro USB

## Slide 18: Arduino UNO Rev3 Schematic
USBConnector
ICSP Connector
MicroController
MicroController
Serial Comms
16MHz
16MHz
GPIO
ICSP Connector
Reset Button
3.3V Regulator
Power LED
Power Connector
5V Regulator
Converts USB to RS-232 Serial
General Purpose Programming
Serial Comms LEDs

## Slide 19: ATmega328P 28-pin DIP Pinout

## Slide 20: Atmel AVR Atmega 328P Microcontroller
High Performance, Low Power Atmel®AVR® 8-Bit Microcontroller Family
  Advanced RISC Architecture
  131 Powerful Instructions – Most Single Clock Cycle Execution
  32 x 8 General Purpose Working Registers
  Fully Static Operation
  Up to 20 MIPS Throughput at 20MHz
  On-chip 2-cycle Multiplier
High Endurance Non-volatile Memory Segments
  4/8/16/32KBytes of In-System Self-Programmable Flash program memory
  256/512/512/1KBytes EEPROM
  512/1K/1K/2KBytes Internal SRAM
  Write/Erase Cycles: 10,000 Flash/100,000 EEPROM
  Data retention: 20 years at +85C/100 years at +25C
  Optional Boot Code Section with Independent Lock Bits
  In-System Programming by On-chip Boot Program
  True Read-While-Write Operation
  Programming Lock for Software Security
http://www.atmel.com/images/Atmel-8271-8-bit-AVR-Microcontroller-ATmega48A-48PA-88A-88PA-168A-168PA-328-328P_datasheet_Complete.pdf

## Slide 21: Atmel AVR Atmega 328P Microcontroller
Peripheral Features
  Two 8-bit Timer/Counters with Separate Prescaler and Compare Mode
  One 16-bit Timer/Counter with Separate Prescaler, Compare, and Capture Mode
  Real Time Counter with Separate Oscillator
  Six PWM Channels
  8-channel 10-bit ADC in TQFP and QFN/MLF package
  6-channel 10-bit ADC in PDIP Package
  Programmable Serial UART
  Master/Slave SPI Serial Interface
  Byte-oriented 2-wire Serial Interface (Philips I2C compatible)
  Programmable Watchdog Timer with Separate On-chip Oscillator
  On-chip Analog Comparator
  Interrupt and Wake-up on Pin Change

## Slide 22: Atmel AVR Atmega 328P Microcontroller
Special Microcontroller Features
  Power-on Reset and Programmable Brown-out Detection
  Internal Calibrated Oscillator
  External and Internal Interrupt Sources
  Six Sleep Modes: Idle, ADC Noise Reduction, Power-save, Power-down, Standby, and Extended Standby
I/O and Packages
  23 Programmable I/O Lines
  28-pin PDIP, 32-lead TQFP, 28-pad QFN/MLF and 32-pad QFN/MLF
Operating Voltage:
  1.8V to 5.5V
Temperature Range:
  -40C to +85C
Speed Grade:
  0 - 4MHz@1.8 - 5.5V, 0 - 10MHz@2.7 - 5.5.V, 0 - 20MHz @ 4.5 - 5.5V
Power Consumption at 1MHz, 1.8V, 25C
  Active Mode: 0.2mA
  Power-down Mode: 0.1μA
  Power-save Mode: 0.75μA (Including 32kHz RTC)

## Slide 23: Different Atmega Microcontroller Memory Options

## Slide 24: Block Diagram
Multi-purpose pins

## Slide 25: Lab#1
The Lab Materials list has been posted on Canvas.
Lab#1 has been posted on Canvas.
Since you will need to order components, Lab#1 will be due at midnight on 10/19/21.
Your assignment for this week is to order the components so you can start working on the lab next week.
If you want to work at home or on a laptop, make sure your have the Arduino IDE installed.

## Slide 26: Lab#1
In this lab, the student will build an ATmega328P based microcontroller system on a breadboard, connect basic peripherals to allow the microcontroller to boot and execute basic Arduino sketches. Students will download software and confirm that the breadboard version of the microcontroller works exactly like the printed circuit board version of the ATmega328P included with the Arduino UNO or Spark Fun RedBoard.

## Slide 27: Lab Reports
Each Lab is worth 12.5% of your overall grade.
Each Lab will be graded on a 100 point scale.
Make sure you answer every question stated in the Lab Descriptions and complete every time in the checklist included with the Lab.
All Lab Reports will be due at Midnight one week after they are assigned (Lab#1 and Lab#8 are the only exceptions).
Late Lab Reports will be penalized 5 points per day late.
All Labs should be submitted on Canvas. Please do not email your Lab Reports to the instructor.
Lab Reports should be submitted as a single PDF document with all software included as an appendix.

## Slide 28: Lab Reports
Make sure to include oscilloscope and/or logic analyzer screenshots with your Lab Reports.
Add labels so that your writing can be clearly related to the waveforms.
Example

## Slide 29: Next Week
Programming in Arudino "C"
  Data Types and Variables
  setup() and loop()
  Programming Structures (conditional statements, loops, functions)
  Bitwise operators, masking, shifting
  Comments
Arduino Integrated Development Environment (IDE)
  Compiling and downloading code
Arduino Libraries
  Including Libraries
  Example “Sketches”
Optiboot Bootloader
WinAVR Tools
  avr-gcc, advdude