## Slide 1: Introduction to Microcontrollers Fall Term, 2021
Professor Allan Douglas

## Slide 2: Lecture Outline
Microcontrollers Everywhere!
Wi-Fi 802.11
Wi-Fi Module - ESP8266
Level Shifter and Linear Regulator
Updating ESP8266 Firmware with the FTDI Board
Wi-Fi Module Library and Operation
Lab#8

## Slide 3: Microcontrollers Everywhere!
We have already discussed the fact that every IR remote has a microcontroller inside. Three years ago, we had IEEE Tech Teardown. All the participants performed experiments with Microwave ovens. They we tore them apart to find out how they are made. There is a microcontroller inside!
4-bit Microcontroller

## Slide 4: Microcontrollers Everywhere!
Also, last year I was troubleshooting in a problem with my pellet smoker (getting ready for turkey day). Here is a picture of the controller for a Traeger smoker.
Microcontroller

## Slide 5: Schedule/Labs
Lab#7
  Due by midnight
Lab#8 has been posted on Canvas
  Due 12/14 by midnight

## Slide 6: Wireless Connectivity
Wi-Fi is short for Wireless Fidelity.
A wireless transmitter, or hub, is required; this device
receives information from the internet via your home
broadband connection. This transmitter (often referred
to as a Wireless Access Point, or WAP) then converts this
information into radio waves and emits it, effectively creating a small, local area around itself, within which your devices can receive these radio signals if they are fitted with the correct kind of wireless adapter.
This area is often termed a Wireless Local Area Network, or WLAN for short.
The radio signals aren’t very strong, which is why the Wi-Fi signal doesn’t travel very far; it will travel far enough to cover throughout the average home and to the street directly outside, for example, but not much further. One wireless hub is usually enough to enable you to connect to the internet in any room in your home, though the signal will be stronger the nearer the hub you are.

## Slide 7: Wi-Fi Standards
http://www.l-com.com/blog/post/2017/07/20/Standards-Showdown-80211-Standards-Side-by-Side.aspx

## Slide 8: Wi-Fi Module ESP8266
The ESP8266 Wi-Fi Module is a self contained SOC with integrated TCP/IP protocol stack that can give any microcontroller access to your WiFi network.
The ESP8266 is capable of either hosting an application or offloading all Wi-Fi networking functions from another application processor. Each ESP8266 module comes pre-programmed with an AT command set firmware, meaning, you can simply hook this up to your Arduino device and get about as much WiFi-ability as a WiFi Shield offers.
Features
  802.11 b/g/n
  Wi-Fi Direct (P2P), soft-AP
  Integrated TCP/IP protocol stack
  Integrated PLLs, regulators, DCXO and power management units
  +19.5dBm output power in 802.11b mode
  Power down leakage current of <10uA
  1MB Flash Memory
  Integrated low power 32-bit CPU could be used as application processor
  SDIO 1.1 / 2.0, SPI, UART
Microcontroller

## Slide 9: Wi-Fi Module ESP8266
This is a Serial-to-Wi-Fi device.
Using serial TX/RX to send and receive Ethernet buffers, and similarly, using serial commands to query and change configurations of the Wi-Fi module.
This board offloads Wi-Fi-related tasks to the module, allowing your microcontroller code to remain simple.
CH_PD needs to be connected to 3.3V
Note: Some modules labeled as EN
instead of CH_PD
Radio
Antenna

## Slide 10: WiFi Module ESP8266
We need a level-shifter (Logic level converter) to connect to the ESP8266.
  The ESP8266 is a 3.3V part.
  The Arduino IO pins operate from a 5.0V supply.
  You will need to solder pins for your breadboard.
Note, you will also need a 3.3V regulator. (Use LD117V33 that came in the Jameco “Build Your Own Arduino” kit).

## Slide 11: ESP8266 Firmware Update: Wiring
The Arduino 3.3V pin will not supply enough current for the 8266 IC. Use an external linear regulator to generate 3.3V from 5V.
Use a level shifter to connect the 3.3V RX/TX signals of the 8266 to the 5V RX/TX signals of the FTDI board.
Connect the ESP8266 CH_PD (or EN) pin to the 3.3V power supply pin.
Make sure that all components share a common ground.
Connect the 5V FTDI board to the level shifter high-voltage RX/TX pins.

## Slide 12: ESP8266 Firmware Update: Wiring
ESP8266 CH_PD pin to the 3.3V power supply pin (if soldering)
Can use female to male jumper wires instead.
Wiring Note:
Be sure to carefully examine your ESP8266 module pin-out and pin labels. They may not all be the same.
The Tx from the FTDI board needs to connect through the level shifter to the pin labeled Rx on the ESP8266 module.
Similarly, the Rx from the FTDI board needs to connect through the level shifter to the pin labeled Tx on the ESP8266 module.

## Slide 13: ESP8266 Firmware Update: Wiring
If you solder a 2x4 header to the ESP8266, you can use color coded wire to connect the device to your breadboard.
You should consider
making a table like this
to make the wiring easier.

## Slide 14: Update ESP 8266 Firmware
Connect the ESP8266 to the FTDI breakout board using the previous wiring diagram.
Connect the FTDI to your computer using USB.
Open TeraTerm (free download) and make the following setup changes to the terminal and serial port.
Verify that you have the
5V version of the FTDI

## Slide 15: Update ESP 8266 Firmware
Disconnect the 3.3V and CH_PD (or EN) pins on the ESP8266, reconnect them, then type “AT” at the console window.
“OK” Should be echoed back to the console if the chip is connected properly.
Note: Reference Link for AT Command Usage:
https://room-15.github.io/blog/2015/03/26/esp8266-at-command-reference/

## Slide 16: Update ESP 8266 Firmware
Disconnect the CH_PD (or EN) and 3.3V pins from 3.3V power again. Connect the GPIO0 PIN to ground and re-connect the CH_PD (or EN) and 3.3V pins to 3.3V power. This should put the chip into boot mode.
Download nodemcu flasher master zip file from Canvas. Unzip, and open the nodemcu flasher (nodemcu-flasher-master\Win64\Release\ESP8266Flasher.exe
Download v0.9.2.2ATFirmware.bin from Canvas.
In the config menu of the nodemcu firmware programmer, select the first setting, then navigate to the v0.9.2.2 AT Firmware.bin file.

## Slide 17: Update ESP 8266 Firmware
Make sure TeraTerm is closed.
Select the flash button in the operation menu to program the device (should take a few minutes). If you do not see progress bar: select stop, check connections and start again.
After flashing is complete, disconnect the CH_PD (or EN) and VCC Pins from 3.3V. Disconnect the GPIO0 pin from ground (can leave floating) and re-connect the CH_PD and VCC pins to 3.3V.

## Slide 18: Update ESP8266 Firmware
Open TeraTerm, type “AT” at the TeraTerm terminal window to verify that the device is operational. (“OK” should be echoed back to the console.)
Type “AT+GMR” to check the firmware version. You should see “0018000902”. The firmware was successfully updated.

## Slide 19: Wi-Fi Sketch

## Slide 20: Changing your SSID and Password
Need to change
this line.

## Slide 21: Lab#8
  Lab Overview
  The objective of this lab is to interface the microcontroller with a ESP8266 Serial-to-WiFi device and create a small web server.
  Part1: Soldering
  Solder pins to your level-shifter and to the ESP8266. You can solder wires to the ESP8266 if you prefer.

## Slide 22: Lab#8
Part2: ESP866 Firmware Update
Follow the instructions presented in this lecture. You will need to download files from Canvas and connect the ESP8266 to the FTDI board you used in the “Build You Own Arduino” kit.
Verify that you have the correct firmware loaded on the ESP8266 before you proceed.

## Slide 23: Lab#8
Part3: Arduino Sketch for WiFi Server
The following figure shows the complete circuit you need to build for this part of the lab.
For this part of the lab you can use the WiFi.ino sketch included in the Canvas folder.
Note, you will need to change the code on line 49 to your wireless network SSID and Password.
Also, this sketch uses microcontroller memory very inefficiently. You will notice a message stating “Low memory available, stability problems may occur.” This is normal and has not caused problems in any testing so far.

## Slide 24: Lab#8
Open the Serial Monitor and set the baud rate for 9600. When you have everything connected properly, you should see the following output:
The wireless network must be running DHCP in order to assign the Wi-Fi module an IP address. In this example, the IP address that was assigned is 192.168.1.102. This example uses a wireless router with SSID=OITGuest and Password=DEADBEEF.

## Slide 25: Lab#8
At this point, the microcontroller is waiting for a client to connect and request a webpage.
Use a PC or your cell phone to connect to your wireless network and open a browser to IP address 192.168.1.102. You should see the microcontroller send status information to the serial port as soon as the browser requests the webpage.

## Slide 26: Lab#8
The webpage displayed in the browser should look like:
Enter your name in the text entry box and click submit. The microcontroller should generate a new webpage, display your name (text you entered), and the number of times the webpage has been requested. The output will look similar to the following figure.
Enter your name,
click submit, and a
new webpage is
generated and sent
To your browser.
A video titled ESP8266 has been
uploaded to Canvas to help you
with this lab.